Visual Inspection Sheet

Checked all parts were secured to the wall and 				✓

ceiling without any movement.

Couplers are attached tightly to conduit and 					✓

secured to fixings with no movement.

Check for any damage to cable insulation.					✓

Cable insulation of the correct colours used for

conductor identification.

Checked cable routing to ensure all wiring is running 			✓

according to the circuit diagram with no snagging,

kinks or exposed copper.

All conductors in the sockets, switches, consumer 				✓

unit and batten holders were secured tightly with

minimum of copper showing in their correct  position.

Ensured the correct MCB’s are used for relevant circuits.		✓

2 Way Switches are fixed at the correct height of 				✓

1200mm to the top of the switch.

Sockets are fixed in place at the correct height of 				✓

450mm to the bottom of the socket.

Trunking is secured to the wall and levelled and				✓

the trunking lid is locked in place.

No holes present in the outer casings of any equipment 			✓

used after faceplates have been secured back in place.

.